- Introduction

- Agenda

| Day | Time | Activity |
| --- | --- | --- |
| Tuesday 29/8 |  |  |
|  | 10.00 – 12.00 | Introduction and Absolute Accuracy presentation. P25. |
|  | 13.00 – 15.00 | Analysis of wrist and foot. K30 and RML. |
|  | 15.00 – 15.30 | Wrap up. |
| Wednesday 30/8 |  |  |
|  | 09.00 – 12.00 | Investigation of wrist and foot tolerances. |
|  | 13.00 – 13.30 | Discussion of GM proposal. |
|  | 14.00 – 16.30 | Analysis of wrist and foot. K14 and RML |
|  | 16.30 – 19.00 | Wrap up and documentation. |
| Thursday 31/8 |  |  |
|  | 09.00 – 10.00 | Analysis of flange tolerances K3. |
|  | 10.00 – 12.00 | IT Discussion P25. |
|  | 13.00 – 15.00 | Summary of wrist, foot and flange investigation. |
|  | 15.00 – 18.00 | Technical discussion (Slocum). K4 and RML. |
|  | 19.00 | Dinner at Pråmen. |
| Friday 1/9 |  |  |
|  | 09.00 – 09.15 | Introduction. Conference room K12. |
|  | 09.15 – 10.15 | MIT concept presentation (Slocum). General discussion. |
|  | 10.15 – 10.45 | Coffee. |
|  | 10.45 – 12.00 | Wrist and flange mounting (Willoughby). Foot mounting (Hart). General discussion and definition of priorities. Evaluation and mitigation of technical risks. |
|  | 12.00 – 13.00 | Lunch – guest dining room. |
|  | 13.00 – 13.45 | Experience from Volvo (Axelsson). Clarification of problems and requirements. |
|  | 13.45 – 14.30 | Continuation of wrist, foot and flange discussion. |
|  | 14.30 – 15.00 | Coffee. |
|  | 15.00 – 16.00 | Definition of total project plan, activities and timeplan. |
|  | 16.00 – 18.00 | SEROP – SECRC – MIT discussion session. Parallel kinematic robot structures (Brogårdh). PhD opportunities (Robertson). |
|  | 18.00 | Adjourn. |

- Attendees

MIT

Professor Alexander Slocum

Patrick Willoughby

John Hart

SECRC

Dr Chan–Yuan Gu

Volvo

Stefan Axelsson

SEROP D, R

Dr Torgny Brogårdh

Dan Rylander

Björn Näslund

Per Lindblom (replacement for Christer Lundström)

Sara Lundström

John-Erik Snell

Henrik Jerregård

Alec Robertson

- Kinematic couplings

Details regarding the kinematic coupling concept can be found in various presentations at the following site:

site: www.pergatory.mit.edu/abb

login name: abb

password: BAAABB

Files: 	“Kinematically Coupled Robotics Proposal.doc”

“MIT Project Presentation.ppt”

In general the kinematic couplings represent a mechanical connection technique with repeatability accuracy in the order of micrometres. This allows highly accurate placement and exchangeability of mechanical components. Specific to robot applications, accurate mechanical placement of the wrist unit, foot and flange are the key priorities, responding to demands from customers such as Volvo (wrist replacement) and Ford (accurate foot).

  - Foot and wrist exchangeability

Projects are to be undertaken, for exchangeability of the wrist and foot, by MIT students Patrick Willoughby and John Hart (refer to section 6 for detailed project plans). The information presented by each student, including key points to be addressed, is inserted as follows.

In summary, the wrist mounting method could comprise a kinematic wavy spring washer or a quasi-kinematic coupling. Mechanical exchange would then involve exchanging the wrist and downloading new parameters (extra parameters are required for the coupling). This would also require pre-calibration at the SEROP production centre.

The foot mounting method ideally would comprise three canoe balls mounted on a base plate with matching groove insets mounted in the existing robot foot holes. The robot’s static and dynamic loads would be taken by the canoe balls requiring appropriate, dimensioning of the Hertzian contact zone. This produces optimal accuracy which may be far in excess of the level required, hence a cheaper solution could be to use a quasi-kinematic couplings to achieve a more realistic accuracy level. The load bearing capabilities of such a system must also be appropriately dimensioned.

    - Cell alignment

With regards to measurement techniques, in particular the ability to measure the location of the robot base pins; several solutions to the cell alignment problem were presented. Due to the small separation between the robot mounting pins and the base frame origin, the calculation of the base frame is mathematically poorly defined. Small errors in the measurement system can lead to large errors at the robot TCP. Drawing from the ball bar concept, a semi-sphere can be manufactured into the top of each canoe ball without loss of accuracy. A proprietary tool connects to the sphere and accommodates a measurement system reflector. The tool is rotated as per usual spherical fit techniques and the location of the hole determined. As such the positional error of the hole is reduced to the accuracy of the measurement system. In order to further reduce the error, the Leica system can be mounted on a kinematic coupling plate and placed on the robot base. The cell components can forthwith be measured, eliminating the robot base measurement error. Fixture measurement can be improved through the use of similar semi–spheres that are attached upon construction of the line.

    - Concerns raised

- To achieve the desired accuracy the robot needs to be mounted such that the canoe balls take the entire load of the robot. Is there a danger of plastic deformation?

- Will the effect of corrosive substances on the canoe ball foot plate introduce surface cracking, eventually leading to failure? How does dirt and grime affect the mounting accuracy?

- How does temperature effect the accuracy of the mounting? How does this compare to the expected temperature deviation of the robot structure?

  - Other applications

With regards to the use of kinematic couplings elsewhere in the robot structure, several components were identified.

- The Voyager base should be converted to a three point mounting to optimise accuracy. The existing four point mount is not an appropriate solution for accuracy based applications. An alternative is to introduce a fifth mounting point at the front of the Voyager base. According to the Voyager team, this should not be a problem in the future.

- Mounting of axis-2 cover plate. Currently achieved with 10–15 bolts on the IRB6400R machine. It would be possible to use three quasi-kinematic coupling “plugs” to accurately place the cover. Shear stresses would be taken by the three bolts (typically through the plugs) as well as the plugs themselves that are inset into the robot structure. A watertight seal is not guaranteed for a three point mounting requiring a rubber gasket to be inset as per standard engine construction techniques.

- Connection of the wrist unit is currently achieved with 8 bolts. This could also be achieved with three quasi-kinematic coupling plugs, but it must be determined whether three bolts are sufficient to take the bending load. The three plugs would take the shear stresses, together with the bolts. According to the mechanical design engineers, at least six bolts are typically required.

- Use of kinematic couplings elsewhere in the structure where accurate and repeatable mechanical interfaces are required.

- Volvo’s Experience

A summary of Volvo’s experiences indicates that they achieved exchangeability of robot components for the Kuka spot welding and handling robots. Exchangeability of the wrists is made possible through the accurate mounting interface (two control pins) and the same accuracy parameters (Kuka wrists are manufactured to be exchangeable). The foot is also sufficiently accurate to allow the exchange of an entire robot. The accuracy demands following such actions are diminished, with an acceptable positioning error of 2–3mm.

Volvo feels that the optimum future solution for Absolute Accuracy maintenance is to use mechanically exchangeable parts, without the need for re-calibration. Use of a measurement system can result in maintenance time of six to twelve hours, compared with one half hour at best for mechanical exchange. However, if a measurement system were efficiently integrated into the robot cell (i.e. ABB provide an entire cell instead of single robots) then this could also be an effective solution.

- Project plan

  - Exchangeable robot foot — John Hart

- Investigate and document existing tolerances in robot base IRB6400 and IRB6400R. Development of CAD models. September 2000.

- Conduct customer (GM) interview(s) to determine correct base frame alignment strategy. Align to axis 1 or align to base mounting pins? Present in conjunction with Absolute Accuracy slides. December 2000.

- Identify first phase alternatives for base mounting system. Define design criterion (cost, ease of use, customer requirements, performance, etc.) for each alternative. November 2000.

- Flexural couplings.

- Standard canoe ball.

- Quasi–kinematic coupling.

- Develop and construct prototype base for chosen kinematic-coupled base (without need for robot) to perform repeatability and other criterion. Integrate simulation information from ADAMS models regarding interface torques and forces, now and future. January 2001.

- Develop retrofit base structure for robot structure (IRB6400 or IRB6400R) and test on site at ABB Robotics, for repeatability and other criterion. Measurement using Leica for static and dynamic exchangeability accuracy. Requires specific Robotics resources. June 2001.

- Implement pilot installation (test cell) at GM Detroit for Absolute Accuracy, CalibWare and kinematic coupling. August 2001.

- Advance purchase of robot for GM cell, November 2000.

- Investigate and develop appropriate software administration mechanism for robot error parameters, specifically for the GM customer demands (refer to separate document). Investigate possibility for integration into the ABB Absolute Accuracy CalibWare software product (MITWare?). August 2001.

  - Exchangeable wrist unit — Pat Willoughby

- Investigate and document existing tolerances in robot wrist IRB6400R. Development of CAD models. Investigation of Absolute Accuracy wrist and overarm parameters. Integrate simulation forces at interface between wrist and overarm. ABB supplied from ADAMS models. November 2000.

- Identify alternatives for coupling system. Define design criterion (cost, ease of use, customer requirements, performance, etc.) for each alternative. December 2000.

- Flexural couplings.

- Standard canoe ball.

- Quasi–kinematic coupling.

- Spring washer.

- Retrofit wrist adapter. May 2001.

- Develop and construct retrofit robot wrist adapter for chosen alternative. Implement on separate test jig (without need for robot) to perform repeatability tests.

- Implement and test on detached extension–wrist unit (obtain from USFAC).

- Implement and test on full robot system at ABB Robotics. Requires specific Robotics resources.

- Improved design wrist unit. August 2001.

- Investigate potential for reduced number of bolts, considering bending and torsional effects.

- Changes to casting/manufacturing drawings.

- Weak link for predictable failure mode, in wrist or tool?

- Kinematic couplings for extensions.

  - WonderWyler unit — Pat Willoughby

As an additional application of kinematic couplings, the WonderWyler unit was presented to Slocum et al. Refer to separate documentation for concept and specification definitions. MIT will design and construct a prototype unit. Refer to WonderWyler project plan for further details.